## Slide 1
TeraSci Test Systems
Site Communication Outline

## Slide 2: TeraSci Internet Infrastructure
TeraSci currently supports over 50 WW sites
  Each site connect back to TeraSci via the Internet
    Each site has its own independent Server
    See slide Internet WAN Traffic for our security model
  The Site Server supports any number of test platforms
    Sites can be 1 test platform to as many as needed
    See individual PPT’s for each Platform details
TeraSci HQ server farm supports
  DB Central – see slide DB Central for details
  TeraSci Portal – see slide TeraSci Portal for details
See the diagram below for a overview schematic

## Slide 3: TeraSci Internet Connections
TS
Engineering
Test Record
Database
TeraSci
Central DB
Site 1
Site 2
Site 3
Site n
Customer
Portal

## Slide 4: TeraSci DB Central
DB Central is a collection of servers at HQ
  This includes:
    Physical Servers
    Virtual Servers
    Linux Containers
    Storage servers
  Site Data is R-sync’d to DB Central in real time
  TeraSci proprietary software package tsTracker
    Manages all data from the sites to an aggregated SQL DB
    Hosts the TeraSci Portal for customer access
    Scrubs and validates hosted data

## Slide 5: TeraSci Portal
TeraSci Portal (www.terasci.com /portal)
  The Portal provides a 24/7 access to the relevant data
      Our Partners: Engineering / Production / Planning / QA teams
      Sites: Engineering / Production / Planning / QA teams
      Drive manufacturer’s: Engineering / QA / RTV teams
  The Portal contains
      Access to all platform data from all sites
      Custom reports for each of our users (by function)
      Automated reports for proactive data mining
      All TeraSci documentation for online access
      Data Freshness to see the the last updates
  Portal Access is restricted to Specific Entities
      Access is via Username & Password
      Users are restricted to only their data

## Slide 6: TeraSci Site Deployment
Site traffic starts at the Site Server
  1st ethernet port (WAN) to the Internet & back to TeraSci (secure access)
  2nd ethernet port (LAN) to the test platforms (via site infrastructure)
Site Server Functions
  MySQL Database
  NFS File Server
  SSH passthrough to all platforms
  Site Server Hosts the WIP Ship function
See diagram below for the schematic overview

## Slide 7: TeraSci Site Deployment
TeraSci Site Server
HDD/SDD 1
HDD/SSD 2
PSU
ODD
Battery
Galileo GUI
HDD Test Rack
HDD Test Rack
SSD PCIe
Tablet
HDD USB
WIP Ship
SSD NVMe
Whole Unit
Internet

## Slide 8: Internet WAN Traffic
TeraSci Internet security requirements
  Site must open 1 outbound port
  Outbound port will connect only to the TeraSci IP
  Site should not open any inbound ports
Communication is via reverse SSH tunnel
  Communication is established by the site server back to HQ
    Site Server and HQ paired Container are Linux based systems
    Site Server can only connect to the paired server at HQ
      Com traffic is secured via unique shared keys
      Com traffic is restricted to Point to Point connection

## Slide 9: Site Ethernet Infrastructure
Server to platform communication is via site infrastructure
  Site provides a VLAN for TeraSci traffic (security)
  Site Provides Cables and Switches from Site Server to work area
Test Platforms are computers running Linux Debian
  Each test platform must connect back to the Site Server
    Network traffic: 2K to 5K Text files, typically less than 50K bytes per hour
  All test platforms support SSH sessions
    TeraSci engineering uses SSH for:
      Remote training, operator support & operator monitoring
      Remote troubleshooting & maintenance of the hardware
      Remote software updates, debug & product troubleshooting

## Slide 10: TeraSci Test Philosophy
To achieve High Volume, High Quality, Low Cost
  Systems must be managed via a Database
    There is never enough data to solve every issue
    Test platforms are data collection systems
    Most software updates are to collect additional data
  Test Platforms must be at the same revision levels WW
    Updates of Software and Parametric tables must be automated
  WW data must be aggregated to a single DB
    Data mining must be proactive and automated
  Final Pass / Fail criteria & disposition must be DB controlled
    Operator decisions must be minimized

## Slide 11: Commodity Level Reports
Each commodity must have unique reports
  Automated reports to be proactive
    Test Hardware Health Monitoring
    Test software detected faults
    Operator Productivity and Quality
    Yield Analysis & FA must be very detailed
      Generalized Yields for day to day tracking
      Detailed analysis by pareto
  Standard reports for engineering review
  Ad-Hoc reports to deep dives

## Slide 12: Revision Controls
Test revisions the same across all sites/customers/platforms
Binary code revision controls for TeraSci hardware
Firmware revision controls for commodities (Drives, Phones, Motherboards, etc.)
Project (Whole Unit, MAC, Phones, PXE, Android, Busy Bee, Mobile, Debian) Git Controls
AVL (PID, MPN, CPN, HP PN, Lenovo PN, etc.)
Hardware Revisions, Date Code & Lot Code Checks

## Slide 13: Automated Analysis & Monitoring
0 Yield & Low Yield checks
High DNR checks
FW revisions vs Master Data
Master Data cross validation (Central vs Site)
Routing Checks (FGI, DGI, Scrap, OOW, etc.)
DMESG, FTP, Hardware/Software Health Monitoring, RAID Health
Logs analysis (Watcher, FTP, Drive, etc.)
Weekly/Monthly Yield Trends
Test Station / Port Failure Rates
Operator Comments & Pass/Fail Rates

## Slide 14: WIP Ship
Customer Specific Requirements
Serial Number Validation (internal vs external check, format, matches test)
Fraud Checks
Repeat Returns
Generate Flat Files (CSV, XML, etc.) and System Link requirements
Forced Routing (can’t route a fail as a pass, or untested part)
Proper Tester (SAS vs SATA vs NVME) – Similar connectors, different platforms
Ensure all data collected and in proper format
Validation against Master Data
SSD Life / Wear Check (in addition to the test)
Automated QA
Engineering Holds (Failure Analysis, Investigations, etc.)
Customer Captures
Final VMI (Visual Mechanical Inspection)
Produce Erase Record for Storage Commodities

## Slide 15: Datamart Services
Sites / Customers upload 3rd Party (non-TeraSci) data
  Data Destruction, Receiving, DOA, Customer Calls, etc.
TeraSci performs validation – rules based processing
  Reject bad records, must be re-uploaded
    Error messages/reasons with details
  Accept good records, move from Stage to Production (accessible on TeraSci Portal)
Maintain contact lists
Provide regular checks (e.g. monthly uploads, missing uploads, summaries of uploads)
Link 3rd Party data to TeraSci Data
End to End Analysis
Raw Reports
Customer Reports
OLAP Cube Available
API Access Available
SQL Read Only Access Available
24/7 Access